## Slide 1
Hg+ ion
Single-atom optical clocks
D. J. Wineland, NIST, Boulder

## Slide 2
Hg+ ion
Summary
Why precise clocks?
Atomic clock basics
Optical atomic clocks
  - atomic ion examples
  (neutral atoms good too)
Why single atoms?
State of play
Future
Single-atom optical clocks
D. J. Wineland, NIST, Boulder

## Slide 3
pulse emitted at t0
pulse received at t1
ℓ
ℓ = c x (t1 – t0)
error: ℓ = c t
for t = 10-9 s, ℓ  30 cm
(t)/(1 day) = 10-14  f/f0
Why precise clocks?
Navigation: e.g. satellite navigation (GPS)

## Slide 4
Global positioning system GPS
satellite network
gives 3 space
dimensions
+ time

## Slide 5
Clocks
Traditional periodic event-generators,
or frequency references:
counter
periodic-event
generator
pendulum clock
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.:

## Slide 6
Atomic energy state superpositions act like pendulum clock
superposition of
electron energy levels,
wave function:
 = |1 + exp(-i2f0t) |2
oscillating electric dipole
plot of electron density vs. time
Planck’s constant
at frequency f0 = (E2 – E1)/h
center
of atom
|1
|2
Energy 

## Slide 7
plot of electron density vs. time
|1
|2
Practical mode of operation:
1. Start atom in |1.
3. Measure probability of | 2.
Maximum | 1  | 2 transition probability when fL = f0 .
2. Apply radiation at frequency fL for short time.
center
of atom
|1
|2
Energy 
superposition of
electron energy levels,
wave function:
 = |1 + exp(- i2f0t) |2
oscillating electric dipole
Planck’s constant
at frequency f0 = (E2 – E1)/h
Atomic energy state superpositions act like pendulum clock

## Slide 8
detector
radiation source
frequency f
electronic feed back servo
counter
Atomic clock recipe
f 
f0
transparent cell (“trap”)
containing atoms
absorption 
1
2

## Slide 9
Why atomic clocks?
Pendulum:
ℓ
f = [g/ℓ]1/2/2
Environmental sensitivity:
(e.g. temperature T)
f/f0 = - ½  (T)
coefficient of thermal expansion:
ℓ = ℓ  (T)
low expansion materials:  ~ 10-8/◦C
 f/f0  -5 x 10-9/ ◦C
gravitational
acceleration
Reproducibility:
f0 depends on:
 manufacturing tolerances (ℓ)
 local value of g
 wear
Atoms:
Reproducibility:
 all atoms of a particular kind
(e.g., 133Cs ) are identical!
 atoms don’t wear out!
Environmental sensitivity:
(e.g. temperature T)
relativistic time dilation:
(f0(T) – f0(T = 0))/f0 = -½(v/c)2
 -1.4 x 10-13 T/M(u)
For M = 133 u (e.g., 133Cs – Cesium)
f/f0  -1 x 10-15/ ◦C

## Slide 10
 -wave cavity
(Ramsey method)
-waves
atomic beam
 f ~ 1/(2Ttransit)
e.g., Cesium beam clock (hyperfine trans.)
f0 ≡ 9 192 631 770 Hz (microwaves)
e.g., NBS-6 (~ 1976)
L = 3.75 m,  f  30 Hz (Ttransit ~ 16 ms)
state detection
(e.g., state-dependent
fluorescence)
state preparation
(e.g. laser optical pumping)
count
atoms
f0
absorption 
Atomic beam spectrometer
f = 1/(2Ttransit)

## Slide 11
 -waves
state detection
(e.g., state-dependent
fluorescence)
state preparation
(e.g. laser optical pumping)
atomic beam
 -waves
atom cooling,
state preparation & detection
Atomic fountain
Atomic beam spectrometer
f0
absorption
 f = 1/(2Ttransit)
NIST F-1
 -wave cavity
(Ramsey method)
count
atoms
Ttransit  1 s

## Slide 12
tick rate can be fast; e.g., for 199Hg+ ( 2S1/2  2D5/2)
f0 = 1 064 721 609 899 144.94 (97) Hz
absorption range very narrow
e.g., for 199Hg+ , f0  1.6 Hz
From 1879 text written by Thompson (Lord Kelvin) and Tate,
(Idea attributed to Maxwell)
``The recent discoveries … indicate to us natural standard pieces of matter such as atoms of hydrogen or sodium, ready made in infinite numbers, all absolutely alike in every physical property. The time of vibration of a sodium particle corresponding to any one of its modes of vibration is known to be absolutely independent of its position in the universe, and it will probably remain the same so long as the particle itself exists."
W. F. Snyder, “Lord Kelvin on atoms as fundamental natural standards
(for base units)” IEEE Trans. Instrum. Meas., 99, 1973.
Why optical atomic clocks?

## Slide 13
199Hg+
1 mm
2S1/2
2D5/2
“trap” electrodes
282 nm
 = 0.1 s
Hg+ ion optical clock experiments at NIST (1981  )

## Slide 14
1 mm
2S1/2
2D5/2
“trap” electrodes
 = 0.1 s
Why just one ion? (single ions  smallest systematic errors)
for two ions,
quadrupole shift ~ 1 kHz

## Slide 15
199Hg+
1 mm
“trap” electrodes
194 nm
Single Hg+ ion optical clock experiments at NIST,1981 
2S1/2
2P1/2
Laser cooling
Hg+
194 nm
Single Hg+ ion

## Slide 16
199Hg+
1 mm
2S1/2
2D5/2
“trap” electrodes
282 nm
 = 0.1 s
Single Hg+ ion optical clock experiments at NIST,1981 

## Slide 17
1 mm
2S1/2
2D5/2
2P1/2
“trap” electrodes
194 nm
cooling
and detection!
Hg+
Detection:

## Slide 18
199Hg+
1 mm
2S1/2
2D5/2
2P1/2
“trap” electrodes
194 nm
Hg+
Detection:

## Slide 19
2S1/2
2D5/2
2P1/2
Hg+
“trap” electrodes
1 mm
atom in 2S1/2 state
atom in 2D5/2 state

## Slide 20
suppresses ion loss (Tstorage ~ 6 months)
suppresses heating, perturbations
from collisions
reduces blackbody radiation shifts
trap
imaging
lens
Ion “trap” in vacuum at liquid Helium temperature ( 4 K)

## Slide 21
averaging time
= 20 s
proximity sensors
laser stabilization:
 = 563 nm
2-mirror resonant cavity:
distance = integer number of
half- wavelengths
Brendt Young, Flavio Cruz, Wayne Itano,
Jim Bergquist , PRL 82, 3799 (1999) + ICOLS ‘99

## Slide 22
t
E(t)
synchronize carrier phase with pulse phase
Frequency domain
f
fr
0
I(f)
f1
f2
f2 = 2 f1
f1 = M fr
!
X 2
feed back on
laser to make
fbeat  0
fbeat
Mode-locked laser
T. Hänsch, J. Hall et al.
Frequency counters, > 2000

## Slide 23
trapping  first-order Doppler shift  0
laser cooling  time dilation small
trapping in high vacuum at 4 K
 small environmental perturbations (collisions, black body shifts, etc.)
Single 199Hg+ ions for (optical) clocks:
J. C. Bergquist et al., (NIST)1981 
 first clock with systematic uncertainly (7x10-17) below Cesium
- W. H. Oskay et al., Phys. Rev. Lett. 97, 020801 (2006)
Jim Bergquist
2S1/2
2D5/2
2P1/2
Hg+

## Slide 24
• trapping ⇒ first-order Doppler shift → 0
• laser cooling ⇒ time dilation small
• trapping in high vacuum at 4 K
⇒ environmental perturbations (collisions, black body shifts, etc.) small
Jim Bergquist
⇒ first clock with systematic uncertainly (7x10-17) below Cesium
- W. H. Oskay et al., Phys. Rev. Lett. 97, 020801 (2006)
2S1/2
2D5/2
2P1/2
Hg+
Single 199Hg+ ions for (optical) clocks:
J. C. Bergquist et al., (NIST)1981 
Plus several other ion species:
88Sr+, 171Yb+, 27Al+, 40Ca+, 115In+
see, e.g., A. Ludlow et al., arXiv:1407.3493
229Th3+
(PTB, UCLA
Kuzmich group)

## Slide 25
Al+ “quantum-logic clock” (T. Rosenband, D. Lebrandt et al.)
Coulomb
interaction
2P3/2
2S1/2
(F=2, mF = -2)
(F=3, mF = -3)
25Mg+
Al+
1S0
3P0
1P1
 = 167 nm
 laser-cooled Mg+ keeps Al+ cold
 Mg+ helps to calibrate B2 from all sources
 collisions observed by ions switching places
 ……
Till Rosenband
|Al + |Al  motion superposition  |Mg + |Mg
David Leibrandt
trap at
~ 300 K
 = 280 nm
P. O. Schmidt et al.,Science 309, 749 (2005)

## Slide 26
Example: relativistic effects in measurement
v/c: (“first-order” Doppler shift)
for f/f0 = 10-18  |v| = 0.3 nm/s
 trap vs. probe laser? Remove as in spacecraft ranging
(Bob Vessot, Ed Mattison et al., PRL 45, 2081 (1980))
– ½ v2/c2 : (time dilation shift)
suppressed with laser cooling
gravitational-potential red shift f/f0 =  grav/mc2 = glocalh/c2
 2nd twin paradox
Systematic frequency shifts
Doppler shifts: f/f0 = v/c – ½ v2/c2
with all systematic errors,
uncertainty (27Al+) = 8.0 x 10-18
after 80 years, your twin (at sea level)
would be 1/1000 second younger

## Slide 27
Some fun science:
Clocks and “relativity”
single Al+ ion clock (pre-wristwatch model)

## Slide 28
James Chou with “portable” Al+ clock (clock #1)
(reference clock in adjacent room, clock #2)

## Slide 30
clock #1 raised 33 cm (~ 13 inches)
f1/f2 = 1.000 000 000 000 000 041(16)

## Slide 31
Jun Ye’s group (JILA), Sr neutral atoms in optical lattice:
f/f0(systematic) = 6.4 x 10-18
(B. J. Bloom et al., Nature 506, 71 (2014))
 T  30 mK
PTB, Braunschweig, Germany
 f/f0(systematic) = 3.3 x 10-18
(unpublished)
weak (octupole) transition, laser Stark shifts, …
H. Katori group (Riken) Sr neutral atoms in optical lattice
 f/f0(systematic) = 7.2 x 10-18 (arXiv:1405.4071)
Moving target!
2.4

## Slide 32
Future?
* “Navigation” at < 1 cm scale:
- Measure earth strain – earthquake prediction
- geodesy: map earth via gravitational red shift
* Fundamental science:
- are the strengths of the basic forces really
constant in time?
- possible deviations from Einstein’s
general relativity?

## Slide 33
Shlomi Kotler, Dustin Hite, Katie McCormick ,Susanna Todaro, Leif Waldner, Yiheng Lin, Daniel Slichter, James Chou, David Allcock, Didi Leibfried, Jwo-Sy Chen, Sam Brewer, Kyle McKay
David Hume Ting Rei Tan
Jim Bergquist, John Bollinger, Joe Britton, Justin Bonet, Ryan Bowler, John Gaebler, Andrew Wilson, Dave Wineland, David Leibrandt, Peter Burns, Raghu Srinivas, Shon Cook, Robert Jordens
Not pictured: Brian Sawyer, Till Rosenband, Wayne Itano, Dave Pappas, Bob Drullinger
NIST “IONS” June 2014